Project Name:	Cache Rules Everything Around Me

Summary:	GPS tracking module with a graphic display. In tracking mode, the graphic display outputs the trip average speed, time elapsed, and total distance traveled. While not in tracking mode, the device enters a low power state by reducing current to the GPS and Bluetooth module.

Inputs and Outputs:
- Input:	NMEA 0183, 9600 baud default GPS data stream
- Input:	5V USB charging
- Output:	Graphic display

Specifications:
- Display instantaneous speed while in tracking mode
- Display time elapsed since entering tracking mode
- Display average speed since entering tracking mode
- Display total distance since entering tracking mode
- Is able to store an ordered list of 50 GPS waypoints
- Is able to measure distance from current location to the current waypoint within ﻿±5% for distances between 1 and 10 kilometers
- Sets current waypoint to next waypoint when within 100 meters of the current waypoint

___________________________________________ ___________________________
Sebastian Luy	Date

___________________________________________	___________________________
Andrew Hayford	Date
Feasibility Report

Design
Preliminary design has been completed and several components have been purchased to accelerate the development of the project. The Arduino Fio V3 (ATmega32U4) was selected as a development board to stage the first model of the project. This board supports Lithium Polymer battery power for portability and has sufficient pins to communicate with a display, GPS breakout and Bluetooth module. Additionally, the Fio V3's 1024 byte EEPROM can handle the storage of an ordered list of 50 GPS waypoints as required by the specifications of the project.
For this project, a Nokia 5110 84x48 LCD was selected as the device's display. This display is low-power, a plus for the battery-powered design, and features serial communication. For handling Bluetooth, an Adafruit Bluefruit LE 4.0 was selected. This device can be easily driven by any microcontroller with SPI support, and can be used to communicate with almost any Bluetooth-compliant device. Finally, the GPS module selected in the first model was the Adafruit Ultimate GPS Breakout. This device features update frequencies from 10Hz to 1/10Hz, flash memory which can store over 16 hours of logged data, and only 20mA current draw.
Based on the components selected in the prototype design, it appears as though the conditions of the contract may be met. Primary constraints of concern while developing on the Fio V3 are the ATmega32U4's limited EEPROM storage and relatively small program memory. EEPROM size is relatively simple to manage, however, the small program memory means developed programs will require extensive optimization and removal/minimization of extraneous code.
As this device is intended for exercise and outdoor applications, several commercial alternatives are available from vendors such as Apple and Garmin. Commercial products have varying complexity across the typical price range of $50.00-$300.00. Some are of the same complexity as the project described in this document, while others include difficult-to-implement features such as heart-rate sensors. For many commercial alternatives, hardware and software designs are unavailable to the general public. However, open-source design alternatives are available from hobbyists and popular component suppliers. These designs use varying development kits and selections of GPS peripherals.

Execution
Development of this project is to be directly funded by the group members. Funding opportunities were not directly investigated due to the project's late start and the member's desire for accelerated development. At the moment, the current budget is set such that the total cost to the group will not exceed $500.00. This is expected to be a reasonable limit, as this leaves approximately $350.00 for future improvements or incidentals (see attached Budget). As discussed earlier, purchase of many of the required building blocks for testing a project model has already been completed. An LCD display, desired development board (Arduino Fio V3 – ATmega32U4), GPS breakout, Lithium Ion battery, and Bluetooth module were recently obtained. It is expected from preliminary design that these components, when together, make a minimal prototype for meeting the project specifications. Further hardware required to exceed the project specifications are expected to be relatively easy to obtain from vendors such as Sparkfun or Adafruit. Electrical components are largely available from the on-campus components vendor in the Electronics Laboratory, or likely Digikey if necessary.
Alternative vendors are largely available for many components required for this project (including bluetooth modules, GPS breakouts, general hardware). Having already obtained and tested the Fio V3 with the purchased peripherals with reasonable success, alternative parts are only required for the initial design in the event of component damage or loss. In preparation for this, the budget has already been allocated a $200.00 incidentals/risk management fund to cover unexpected additional costs. As mentioned before, the budget leaves sufficient room for development on a printed circuit board (PCB) or other possible expansions on the project specifications.
Testing of the project can be largely completed with the equipment available to the group members. Designed hardware can be tested in the Electronics Laboratory, and software can be easily debugged and tested from almost anywhere with limited additional equipment. Basic testing for functionality of the purchased components has already been completed. These tests have thusfar verified reading from the GPS, communication through Bluetooth, and display of GPS data to the LCD.

Teamwork
The group members have previously collaborated in the Electronics I, Computer Architecture & Organization, and Digital Signal Processing laboratories with reasonable success. Future collaboration appears largely possible, as the group members share like interests, including but not limited to: The Wu-Tang Clan, Puerto Rico, bananas, and haiku. With classes like ECE101, ECE177, ECE210, ECE275, ECE214, ECE271, ECE331, ECE342, ECE471, ECE473, ECE498, and ECE598, they are definitely prepared for this project. Both group members are reasonably experienced in C (C++ in the Arduino IDE), which is the primary language used with the selected development kit. It is expected that development of the created project will take upwards of 150 hours, with much of the time being dedicated towards gaining sufficient accuracies and the development of a companion web application. Sebastian and Andrew consistently find an excuse to win.

Budget

It is expected that the project will cost no more than $500.00. Several components have already been selected, purchased, and tested for use in an initial model. Together, the purchased materials can create a very basic model which meets the most basic levels of functionality desired. Below is a table which summarizes the budget for the project.

Table 1: Summary of project budget
Component	Cost	Obtained
Fio V3 - ATmega32U4	$34.95	X
Adafruit Ultimate GPS Breakout V3 - 66 channel / 10Hz Updates	$39.95	X
Bluetooth Low Energy (BLE 4.0) - nRF8001 Breakout (v1.0)	$19.95	X
Lithium Ion Polymer Battery - 3.7v 150mAh	$5.95	X
Printed Circuit Board Development	$100.00
Miscellaneous Electrical Components	$50.00
Risk Management & Incidentals	$200.00

As evidenced by the above table, the budget leaves room for improvements allowing for the exceeding of contract specifications.

Description
This document describes the goals and features of the project to be completed in ECE 406. The device to be designed is effectively a wearable GPS module for exercise or outdoor recreation applications. At the simplest level, the module tracks the user's position, distance traveled, instantaneous speed, average speed, and time elapsed over a user-specified period of time. The device additionally features the storage of GPS coordinates for use as waypoints. These waypoints can be stored in a specific order as to design a course of travel, or a single point may be uploaded to track the user's distance from a destination. With these details in mind, the goals of this project include the display of user data, use of waypoints, the calculation of relevant variables, and implementation of a secure web-application.
As specified earlier, the device's most simple function is to track the user's position over time. The device uses these parameters, as will be discussed later, to compute variables of interest to a user participating in an outdoor recreational activity. The attached contract specifies that the device outputs specific parameters to the display while in tracking mode. Tracking mode is a user-instantiated state where GPS data is utilized to gather the user's instantaneous and average speeds while moving, as well as the time elapsed and distance traveled since starting the trip. These four parameters (instantaneous speed, average speed since starting trip, time elapsed, and distance traveled) are output to a graphic display on the device while in this state. The waypoint feature presented in the introduction is active during tracking mode, and thus the distance to the nearest GPS waypoint is also displayed during this period.
The primary goal in the implementation of the waypoints feature is the ability for the user to store an ordered list of at most fifty GPS coordinates. With an ordered list, a user may create a predefined path of travel prior to going for a hike, run, bicycle ride, or other outdoor recreational activity. The previous paragraph states that the distance from the geographically closest waypoint is output to the display while in tracking mode. Once within a specific radius of the current waypoint (within 100 meters), the next closest waypoint is set to replace the current waypoint, and the LCD is updated to display this information. In the same manner as storing a list of waypoints, single waypoints may be stored on the device to track the user's distance to a specific destination over the course of a trip.
With the amount of distance calculations and parameters required, accuracy is of a high concern. Users purchasing a commercially available alternative expect a reasonable degree of accuracy, especially since many products run upwards of $150.00. Of course, the accuracy of the speed and distance parameters rely heavily on the accuracy of the data obtained from the GPS and precision during calculation. As expected, the data stream from the GPS is compliant with the NMEA 0183 standard. Following this standard offers little consequence to cost, performance, or design complexity. Instead, selecting such a device allows for use of a well-documented data format. This standard is professional and assists greatly in the process of parsing and interpreting data. However, this standard does not govern accuracy, and GPS accuracy is not uniform for all commercial modules. To obtain the desired accuracy for the contract's waypoint specifications, a higher quality, more expensive GPS may be required.
In terms of calculation, the GPS device selected for use in this project can determine a user's position within ±3 meters. Over multiple points, this error has a compounding effect which may greatly distort distance calculations from the actual value over long trips. Commercial GPS watches offer distance accuracies between the range of 0.10% and 7.5%. In order to obtain a similarly reliable measure for consumers, an accurate distance algorithm is required. Several algorithms of varying intrinsic accuracy exist for distance, and thus speed. One such method is to compute the differences in the latitudes and longitudes of two GPS points. The Pythagorean Theorem can then be applied to obtain the distance of the direct path between the two points. This method creates a relatively large degree of error for paths with many turns between two GPS points. The effect of this may be minimized by selecting a GPS update frequency that is fast enough to account for intense variations in a path of travel. Another method, which is much more strenuous, is the application of the Haversine formula for the measure of distance traveled across the surface of a sphere. This method accounts for the curvature of the Earth, but may be excessively complicated for the relatively short distances which are expected on the device. This is especially true for cases where the update frequency is relatively fast. Selection of a method effectively comes down to the balance of accuracy with available program memory. The design decision will be made when appropriate as to prevent locking in with an algorithm which may not be appropriate.
The device uses three primary modes of inter-device communication. For one, the project uses hardware serial to communicate with the GPS breakout. The use of serial reduces the wire density of the project on a breadboard, and is relatively simple to implement communication in software. Downsides appear in that simple, hardware serial is asynchronous, which could prevents the use of multiple devices on the same protocol. SPI is used to communicate with both the LCD display and Bluetooth device. SPI offers benefits over serial in that it is synchronous and supports multiple slaves. This is ideal for running both the LCD and Bluetooth breakout. Finally, Bluetooth is a wireless implementation of a serial protocol, and is intended for use in the communication between the device and an Android phone. With the addition of this, an Android/web application may be developed for use along with the project.
The goal with developing a companion application is to allow the user to plot their previous trip using a maps plugin, plot their average speed performances on a given course, and to upload the aforementioned GPS waypoints. This adds a degree of logging and performance monitoring for the user, a feature which is highly desirable in exercise training and conditioning situations. With the introduction of this idea, security becomes an issue. Personal health information is to be stored on the server-side, so protection by user-name and password are required. Additional security measures such as hashing or encryption will likely be implemented. With a reasonable amount security, this project appears relatively harmless. Relatively speaking, the value of the information to be handled on application/server is quite low. It is not expected that a runner's path of travel is information highly desired by those with malicious intent. Regardless of this fact, security is expected to be present for the assurance of the privacy of the consumer's information.
In terms of physical abuse, the device in question is expected to handle the conditions that a typical personal electronic device (mobile telephone) will see. This includes normal temperatures, relatively dry conditions, and minimal abusive behavior from the user. In this respect, some commercial alternatives are found to be shock resistant and waterproof. Given that this project is intended to demonstrate hardware and software design, waterproofing and additional inclement condition protection will not be implemented. The expectation is that the project should be able to withstand outdoor conditions with a moderate amount of movement, as is normal with outdoor recreation.
As mentioned beforehand, this device is largely intended for recreational purposes such as hiking, walking, biking, and running. This device, and it's many commercial alternatives, are largely intended for runners who are interested in their path of movement, distance traveled, and time to complete a given course. In this sense, wearable GPS modules are desirable for their ability to track performance and improvement over a course of time. The goal with the project is to achieve this for a consumer: allow for the measuring and tracking of performance both in real-time (during exercise) and after having completed a recreational activity. Tracking mode on device largely handles the details of a trip during exercise, whereas the Bluetooth connection and Android/web application handle the performance tracking and path plotting.
In terms of work, Andrew and Sebastian intend on dividing the labor for the project on a voluntary basis. Both members have an interest in the subject matter of the project and have similar experience with the components required. With both members having a desire for such a product, division of labor has thusfar been largely effortless. During component selection and testing, Andrew and Sebastian either had worked together to complete the task, or equally divided the work in such a way that division of labor was fair.

Revision Control
Andrew and Sebastian are using git for revision control. The repository currently hold miscellaneous test code for testing on the Arduino, and previously-developed C code for using the Nokia 5110 LCD.